| Worksheet Revision: |  | Serial No.: |
| --- | --- | --- |
| Customer: |  | Completed by/Date: |  |
| Project: |  | Reviewed by/Date: |  |
| SOR No.: |  | Quote No. |  | System Item No.: |  |

Model: 	LKAT2  :  Std.    OEM    Sigma

LKAT+  :  Std.    OEM    Sigma

Mains Power:	 85 to 264VAC (47 to 440Hz) <or> 110 to 264VDC

18 to 36V DC LKAT2 OPTION ONLY

Measurement Head and Cables:	         Actual Bus Size : P1=    mm   P2=    mm                 Mounting Hardware

If LKAT2 P1 is 25…67mm, P2c = P2 + 23mm		       LKAT2 P1/P2   > 68mm

If LKAT2 P2 is 25…67mm, P1c = P1 + 23mm		       LKAT2 P1/P2   < 67mm

Otherwise P1c=P1 and P2c=P2		       LKAT+

‘P’ for Head Calc : P1c=    mm  P2c=    mm

| Nominal Head Size : N1= mm N2= mm |  |
| --- | --- |
| Cable Lengths : | Standard Special |  |  |
| Head ( cables exit head on P1 side ) | 10m m |  |  |
| Output ( except OEM / SIGMA ) | 30m m |  |  |
| Mains Power ( except OEM / SIGMA ) | 10m m |  |  |

| Main / Std. Outputs |  | (“-kA“ not noted for Sigma) | 0% F.S. | Cal.Pt. kA Std. Cal. Pt. is + 100% of F.S. |
| --- | --- | --- | --- | --- |
|  | Main Measuring Range→ | - 100% F.S. - kA | 0kA | + 100% F.S. + kA |
| Output Type Choose One | Current 1 |  | “0 to 20 mA” | -20mA | 0mA | +20mA |
|  | Current 2 |  | “4 to 20 mA” | -12mA | +4mA | +20mA |
|  | Current 3 |  | “4 to 20 mA” | +4mA | +12mA | +20mA |
|  | Voltage 1 |  | “0 to 1 Volt” | -1 Volt | 0 Volts | +1 Volt |
|  | Voltage 2 |  | “0 to 10 Volts” | -10 Volts | 0 Volts | +10 Volts |
| Trip Setpoint 1: | Not Used | Forward | Reverse | kA +/- 5%...100% Main F.S. | DA USE ONLY : NFS : Addendum 046983 |
| Optional “PE” Outputs (Protection Extensions) PE Not Installed | Standard OEM/Sigma 046389 046390 | (“-kA“ not noted for Sigma) | 0% F.S. | Cal.Pt. kA Std. Cal. Pt. is + 100% of F.S. |
|  | PE Measuring Range→ | -100% F.S. - kA | 0kA | +100% F.S. + kA |
| Output Type Choose One | Current 1 |  | “0 to 20 mA” | -20mA | 0mA | +20mA |
|  | Current 2 |  | “4 to 20 mA” | -12mA | +4mA | +20mA |
|  | Current 3 |  | “4 to 20 mA” | +4mA | +12mA | +20mA |
|  | Voltage 1 |  | “0 to 1 Volt” | -1 Volt | 0 Volts | +1 Volt |
|  | Voltage 2 |  | “0 to 10 Volts” | -10 Volts | 0 Volts | +10 Volts |
| Trip Setpoint 2: | Not Used | Forward | Reverse | kA (+/- 5%...100% PE F.S.) |  |
| Trip Setpoint 3: | Not Used | Forward | Reverse | kA (+/- 5%...100% PE F.S.) |  |

Special Instructions

| Optional Display: None | DC (DC Applications) | True RMS (AC or Pulse Applications) 046391 |
| --- | --- | --- |

NOTE : All Comments Corrections and/or Changes Must be Initialed and Dated